## Slide 1: Bio-Inspired Navigation on Varied Terrain
Dexter Shepherd

## Slide 2: Aims of the project
Use inspiration from nature to make a more resilient chassis
Explore methods of enabling an agent to understand its own limitations
Attempt to cross the reality gap from simulated terrain avoidance to physical robotics

## Slide 3: Inspiration
Cockroach locomotion
Project PROLERO

## Slide 4: Genetic approach
Used due to large search space and no training data
Trialled different algorithms and network architectures
  Microbial
  Group evolution
  Conv1D
  Conv2D
  Feed forward
Comparison with rule based approach

## Slide 5: Simulation
Procedurally generated terrain
First person view
Fitness determined by energy and collision

## Slide 6: Simulation results
Performed best with a 2D convolutional neural network
Rule based approach outperformed evolution
Evolved to use contours
Rule based
FNN Microbial
CNN Microbial

## Slide 7: Computer vision
Stereo vision
Pre-processing testing
Off-the-shelf Kinect

## Slide 8: Rule based visual approach
Image cropped to remove depth of floor
Rule based approach finds the least amount of dark pixels

## Slide 9: Crossing the reality gap
Applying trained model on the vision
Visual compression

## Slide 10: Results of crossing the reality gap

## Slide 11: Physical robot implementation
Version 1 – no back bending
Version 2 – Back bending and suspension
Version 3 – Better rotating and improved Whegs
All using the Raspberry Pi Zero

## Slide 12: Proprioception (getting stuck)
Current draw
Standard servo draw of 0.1A
Thresholding (greater than 0.4A)

## Slide 13: Wheg design
3D printed Whegs
CAD designed on SketchUp

## Slide 14: Back bending
Inspired from cockroaches
Evolved solution (hillclimber)
Quick convergence on solution

## Slide 15: Conclusions
Simulation showed proof of concept for evolved navigation
Back bending improved locomotion
Best model was group, however rule based was more trustworthy

## Slide 16: Future work
More compact onboard stereo sensors
Lighter chassis and Jetson instead of Raspberry Pi

## Slide 17: References
Nicholas Tomko, Inman Harvey, Nathaniel Virgo, and Andrew Philippides. Many hands make light work: Further studies in group evolution. Artificial Life, 20(1):163–181, 2014
European Space Agency. Prolero. https://www.esa.int/Enabling_Support/Space_Engineering_Technology/Automation_and_Robotics/PROLERO
R.T. Schroer, M.J. Boggess, R.J. Bachmann, R.D. Quinn, and R.E. Ritzmann. Comparing cock- roach and whegs robot body motions. In IEEE International Conference on Robotics and Au- tomation, 2004. Proceedings. ICRA ’04. 2004, volume 4, pages 3288–3293 Vol.4, 2004.